## Slide 1: Battery-free Wireless Sensing and Beyond
PhD Oral Defense
Swadhin Pradhan
08/04/2020
Advisor: Lili Qiu
Members: A. Mok, M. Gouda, K. Sundaresan
Notes: Good afternoon everyone and thanks a lot for attending my PhD oral defense talk. I am Swadhin and the topic of my proposal is ‘battery-free wireless sensing and beyond’. This work has been advised by Prof. Lili Qiu. I also thank my committee members Prof. A. Mok and Karthik who are present here.

## Slide 2: LOTS of connected devices by 2022
~30 Billion*
*Ericsson Research
Notes: It is evident that Internet of things, i.e., devices or things connected to internet are becoming more and more common place. They surround us and are changing the meaning of physical places. It has been predicted that there will be more than 30 billion connected devices by 2022, according to Ericsson Research.
Gartner Research : ~11.19 Billion …
Ref: http://spectrum.ieee.org/tech-talk/telecom/internet/popular-internet-of-things-forecast-of-50-billion-devices-by-2020-is-outdated

## Slide 3: Missing pieces of massive IoT
Seamless User Interface
  Easily embedded into the environment
Efficient Sensing Modality
  Low physical cost and sensing cost
Deployment friendly
  No need to recharge frequently
  Should be easily discarded or customized
Notes: However, this vision of seamless context-aware smart-spaces is really alluring, there are very few real world realization of this vision. Because, it requires massive IoT deployment and only when, we can truly realize Mark Weiser’s vision of invisible ubiquitous computing. Three main needs of massive Iot are the following.

## Slide 4: Our Approach
Can we use backscattering to realize this ?
Can we use commercial passive RFID tags ?
  Cheap, Customizable, Wireless, Battery-free, Small …
Energy Source
Energy Harvesting
Backscattering Tag
Backscattering
Receiver
Ambient
Backscatter
Notes: Can we use backscattering in which a specific sensing components harvest energy from outside source and uses that for transmitting sensing information. More specifically, can we use commercial passive RFID tags ? This is ne of the major technologies which exploit backscattering to enable communication.

## Slide 5: Challenges to address
How to provide ubiquitous interactivity ?
How to sense beyond translation movement ?
How to sense beyond mobility ?

## Slide 6: Our works
Enabling seamless user interaction
  RIO: A Pervasive RFID-based Touch Gesture Interface
  (ACM MobiCom 2017)
Tracking motion dynamics
  TIMU: Tag-based Motion Sensing
  (In Submission)
Enabling temperature Sensing
  RTSense: RFID-based Temperature Sensor
  (In Submission)
Notes: Toward realizing the vision of turning any physical space into truly context aware, we propose to develop novel approaches and systems that enable battery-free sensing. Three main systems are the following. The main problem-solving approach in all of the three problems are the following: analytical model driven sensing …

## Slide 7: RIO: RFID-based Touch Gesture Interface
Notes: First, we discuss RIO which enable ..

## Slide 8: Can we effectively transform everyday object into a touch Interface ?
Notes: However, the future of IoT demands seamless and intuitive interface between users and the devices. In this setting, we ask that “Can we effectively transform everyday object into a touch interface ?” Can every possible item in our surrounding become a gateway to a possible interaction ? Chair, Table ..

## Slide 9: Our idea: passive RFID tags as touch interface
COTS Tags
COTS Reader/Antenna
Custom Tags
Notes: But how ? To realize this goal of transforming physical object into UI, we re-purpose the use of commercial off-the-shelf passive RFID tags as a touch primitive. We attach the RFID tags into objects as interaction units. We use commercially available reader and antennas to aid that use case. We also build our custom-designed tags to show different other use cases.

## Slide 10
Button
Keyboard
Slider
Dial
Multiple Sliders
Shapes
Notes: More specifically, we are looking at different types of single point touch and tracking. For example, different possible UI units can be Button .. Keyboard .. Slider .. Dial .. Multiple sliders .. And different shapes .. To achieve this we need to perform touch detection, tracking, and tracking within multiple tags ..

## Slide 11
Key Idea and Reasoning
Touch and Single Tag Tracking
Evaluation
Notes: Now, let me delve into the detail of RIO. I will talk through the system following this outline.

## Slide 12
Key Idea and Reasoning
Touch and Single Tag Tracking
Evaluation
Notes: First, let me start with the key idea behind RIO.

## Slide 13
Reader
Antenna
Tag
Finger Swipe
on Tag
Predictable phase change
at reader side
Notes: A RFID system works by sending RF signal and records the backscatter signal to know the amplitude and phase. When user touches or swipes over a passive RFID tag there is a predictable phase change is observed at the reader side.

## Slide 14: Why does it happen ?
ZBody
ZChip
ZAntenna
Induced Current ∝
Backscattered Electric field
and Phase
Notes: Now, let us look at why this thing happens. Every passive RFID tag consists of a chip and antenna. Here, the numbers present the The impedances are presented as .. Human body impedance can also be constructed as Zbody. Induced current in passive rfid tag can be shown as :

## Slide 15
Key Idea and Reasoning
Touch and Single Tag Tracking
Evaluation
Notes: Let’s talk about single tag touch tracking which may enable button, slider, dials and different shape drawing.

## Slide 16: How to detect touch ?
Sudden Jump in Phase
Notes: We observe sudden jump in phase when we touch.

## Slide 17: How to detect tracking ?
Predictable Phase Pattern
Notes: We observe predictable phase pattern which we can exploit to track.

## Slide 18: Single tag tracking algorithm sketch
Phase
Tag Position
Calibration Phase
Last Known
Position
T-second
Swipe Phase
DTW Matching
Potential
New Position
Notes: Now, let’s look at the algorithm sketch. Upper right hand corner shows a demo run if the algorithm. Initially we swipe our finger 3-4 times the calibration phase pattern. .. And then we repeat this process.

## Slide 19
Key Idea and Reasoning
Touch and Single Tag Tracking
Evaluation

## Slide 20: Experimental setup
Camera
RFID Tag
Antenna
Reader
Laptop (Processing)
Notes: We have a camera with opencv to measure the ground-truth.

## Slide 21: Single tag tracking accuracy
Error ~10 mm
Notes: We test the localization tracking error in different speeds of finger movements. And we observe that. Mention Speed.

## Slide 22: Multi-tag tracking accuracy
Error ~18 mm
Notes: If we look at the tag tracking in multiple tags..

## Slide 23: TIMU: Tag-based Motion Sensing
Notes: Good afternoon everyone ! I am Swadhin and thanks a lot for attending my research preparation talk. The title of today’s talk is designing a pervasive RFID based touch gesture interface.. which is based on our recent publication at ACM MobiCom 2017 which was joint work with my Lili and Eugene, Karthik, Amir and Sampath from NEC Labs ....

## Slide 24: Metrics of interest in sports
Ball Motion Analytics in Bat or/and Ball sports
Baseball
Cricket
Basketball
Can be used in coaching and performance improvement

## Slide 25: Different components of ball motion
Linear Speed and Direction
Rotation Speed and Direction
Rotation Axis …

## Slide 26: Can we sense rotation and linear motion with minimal change using single RFID reader antenna ?
Notes: However, the future of IoT demands seamless and intuitive interface between users and the devices. In this setting, we ask that “Can we effectively transform everyday object into a touch interface ?” Can every possible item in our surrounding become a gateway to a possible interaction ? Chair, Table ..

## Slide 27: Our Solution: We exploit polarization property of passive RFID system
Notes: However, the future of IoT demands seamless and intuitive interface between users and the devices. In this setting, we ask that “Can we effectively transform everyday object into a touch interface ?” Can every possible item in our surrounding become a gateway to a possible interaction ? Chair, Table ..

## Slide 28
Key Idea
Evaluation
Algorithm

## Slide 29
Key Idea
Evaluation
Algorithm

## Slide 30: Key Idea
Exploit polarization property of RFID tag with linear antenna
Directly extract the motion states using single antenna
Polarization
Distance
Gain
Notes: K -> Polarization Loss factor (Fixed)

## Slide 31
Key Idea
Evaluation
Algorithm

## Slide 32: RSS Modeling Examples
Notes: First start with rotation axis … and we observe some models..

## Slide 33: Phase Modeling Examples
For a given rotation axis, we get almost unique pattern

## Slide 34: Rotation Axis Estimation Formulation
Model
Rotation Axis
Samples of signal (k)
Notes: Fmincon .. The problem is challenging to solve since the objective is non-linear and has many local optimals. Instead, we
use non-linear optimization (e.g., fmincons() in matlab). We perform the optimization results are sensitive to the initialization. In order
to get good solution, we need an initial solution that is not too far away from the optimal. To improve the speed and quality of the search, we develop
two strategies. First, we use machine learning algorithm to perform initial solution. We use deep neural network (DNN) as the machine
learning algorithm. The advantage of using a DNN is that it can approximate any function with arbitrary accuracy. We use a fully
connected 4-layer DNN, which has 600, 500, 400, and 300 neurons at the first, second, third, and fourth layers respectively. The DNN maps the phase and RSS samples during one rotation to the 3D
rotation axis. Moreover, we observe that searching a rotation axis for each
rotation independently is sub-optimal since it ignores the strong
temporal correlation between consecutive rotations. To take into
account of the temporal locality, for each rotation we generate
multiple initial solutions by injecting a small random noise to the
output from DNNs and feed each of the perturbed solutions and obtain candidate solutions for
each rotation.

## Slide 35: Issue with Initialization
Challenge: Non-linear optimization and easy to get stuck at local minimum
Approach: Develop NN and leverage temporal locality to find good initial solutions

## Slide 36: Rotation axis estimation error
Median error remains within 5 degree

## Slide 37: Rotation speed estimation

## Slide 38: Linear speed estimation
Compensate the
rotation axis and
speed in the
phase to extract
the linear speed

## Slide 39: Algorithm sketch
Denoised RSS and Phase Trend from the RFID Tag(s) attached to a ball
RSS and Phase Template extraction in one rotation
Peak-Valley
Detection
Rotation Axis & Rotation Speed & Azimuth & Elevation estimation
Phase
Compensation
Linear speed, distance & direction from linear phase trend, total change, & slope sign

## Slide 40
Key Idea
Evaluation
Algorithm

## Slide 41: Controlled setup
3D Printed Goniometer
Diff. Rotation Axis

## Slide 42: Controlled setup

## Slide 43: Rotation axis Estimation error
Error remains within 5 degree

## Slide 44: Linear distance estimation error
Median error remains within 1 cm

## Slide 45: Related works of TIMU
IMU enabled Approaches
  Qlipp, Zepp companies ..
IMU with UWB ranging based approaches
  iBall [NSDI 2017]
RFID tracking based approaches (Closest)
  RfIDraw (Custom hardware with multi-antenna for AoA profile) [SigComm 2014]
  RFind (Offline high-bandwidth approach with USRP) [MobiCom 2017]
  Tagyro (Multiple antennas with calibration) [Mobicom 2016] …

## Slide 46: Key takeaways of TIMU
Polarization can be exploited for motion sensing
TIMU can sense different motion states w/o tracking
First RFID-based single antenna motion sensing system

## Slide 47: RTSense: RFID based Temperature Sensing
Notes: In the second piece of work, we build RFID based temperature sensor which can easily be blended with the environment

## Slide 48: Why indoor temperature sensing ?
Users spend around 90% of the time indoors
Indoor personalized thermal comfort is needed
HVAC needs fine-grained real-time knowledge
Notes: Heating, Ventilation, and Air-conditioning system

## Slide 49: Can we measure temperature exploiting impedance change due to temperature variation in RFID tags?
Notes: However, the future of IoT demands seamless and intuitive interface between users and the devices. In this setting, we ask that “Can we effectively transform everyday object into a touch interface ?” Can every possible item in our surrounding become a gateway to a possible interaction ? Chair, Table ..

## Slide 50: Yes! and Key Idea
Temperature variation changes the tag-antenna impedance
  Larger antenna surface area experiences more change
Impedance change manifests in change of reflected signal
Differential sensing of tag-pair used to predict temperature

## Slide 51
Evaluation
Analytical Model

## Slide 52
Evaluation
Analytical Model

## Slide 53: Analytical model
Impedance Modeling of Dipole Tag Antenna
Temperature Impact on Antenna Impedance
Phase Change Modeling from Impedance Change

## Slide 54: Analytical R/L/C model of dipole
R =
+
w
l
d
t
DC Resistance
AC Resistance
Notes: Pro – 1.68*10-8, lambda is the wavelength, f is the frequency, epsilon is the permittivity of air 1.006 …Ansys HFSS meter and LCR meter ..

## Slide 55: Analytical R/L/C model of dipole
Notes: From 8 possible configuration, we choose this which matches the best …

## Slide 56: Temperature impedance model
Larger Width (30cm)
Smaller Width (5 cm)
Notes: VNA measurement versus accuracy with temperature change ... Matches Well …

## Slide 57: Phase impedance model
Distance
Component
Polarization
Component
Antenna Impedance
Component

## Slide 58: Phase impedance model and metric
B
Tag A
Tag B

## Slide 59: Algorithm sketch of RTSense
Calibration Stage
rTagA - rTagB
Temperature
Phase Metric
Tmin
Tmax
Estimation Stage
Mean of 20 Second of data
TPred

## Slide 60: RTSense Tag-pair
Tag-pair based solution
  Battery-free and
  Cheap (~$2)
  Customizable
  Robust against change
Notes: Customizable ..

## Slide 61
Evaluation
Analytical Model

## Slide 62: Oven Iso-temperature setup

## Slide 63: Heat-gun Experimental Setup

## Slide 64: Tag-pair design selection
Larger area induces bigger change

## Slide 65: Related metrics
Analog Identifier (AID)
Differential Minimum
Threshold Power (DMRT)
Phase Difference (PD)
6.2
12.6
2.9

## Slide 66: Impact of distance
Error remains within ~10 degree

## Slide 67: Impact of orientation
Error remains within ~7 degree

## Slide 68: Related works of RTSense
Active RFID based Sensing
  WISP (IEEE RFID ‘07) , Ekhonet (Mobicom ‘14) …
Custom Tag based Sensing
  Gas Sensor (IEEE TMTT ‘13), Humidity Sensor (Sensors ‘12) …
RFID Tag Antenna Sensing (Closest)
  RFID Hacking (Mobicom ‘19), AID (EURFID ‘15) …
Notes: The main issues

## Slide 69: Key takeaways of RTSense
Antenna surface area can be exploited for sensing
Tag-pair based differential sensing can be used for robust approach against environmental changes
RTSense can achieve median error of ~3 degree

## Slide 70: Other published works @UT
[1] Combating Replay Attacks Against Voice Assistants, ACM UBICOMP 2019
  Swadhin Pradhan, W. Sun, G. Baig, Lili Qiu [Audio and RF]
[2] Smartphone-based Indoor Space Mapping, ACM UBICOMP 2018
  Swadhin Pradhan, G. Baig, W. Mao, Lili Qiu [Audio and IMU]
[3] Konark: A RFID based system for enhancing in-store shopping experience, WPA 2017, co-located with ACM MobiSys 2017
  Swadhin Pradhan, E. Chai, K. Sundaresan, S. Rangarajan, Lili Qiu [RFID]
[4] Understanding and managing notifications, IEEE INFOCOM 2017
  Swadhin Pradhan, A. Parate, Lili Qiu, K. Kim [Mobile]
[5] RNN-based Room Scale Hand Motion Tracking, ACM MOBICOM 2019
  W. Mao, M. Wang, W. Sun, Lili Qiu, Swadhin Pradhan, Y. Chen [Audio]
Notes: Apart from these I have these published works including four first author works related to audio sensing, RFID sensing, and mobile sensing.

## Slide 71: Acknowledgement (Collaborators & Members)
Karthik
Eugene
Amir
Sampath
Lili
Ghufran
Wenguang
Mei
Wei
Shuozhe
Abhinav
Kyu-Han
Niloy
Romit
Pradipta
Sourav
Mohamed
Aloysius

## Slide 72: Acknowledgement (Family & Friends)

## Slide 73: Thanks for listening.
Questions ?

## Slide 74: Backup Slides

## Slide 75: Phase and RSS Modeling
Phase
RSS
Gain
Polarization
Polarization
Distance
Distance

## Slide 76: Application areas
Smart Hospitals
Smart Offices
Smart Retail
Notes: With this unprecedented proliferation of IoT, every known physical surrounding is poised to be transformed into the smart and interactive spaces. This transformation is slowly becoming a reality, not only in just home through connected appliances, but in every other imaginable physical spaces: from hospitals to offices to retail. For example, Smart retail space like Amazon Go is enabling seamless automatic check-out and interest detection helping both the shoppers and the shop owners. This is becoming more and more important when we spend more and more time indoors due to this pandemic.

## Slide 77: RTSense overview
RTSense Tag Pair
RFID Reader
Reader Antenna
Ambient Temperature
RTSense Controller
with Temp. Mapping
Impacts Tag Antenna
Impedance
Changes RF Parameters
Phase Difference Information
Predicted Temperature
Notes: Temperature ..

## Slide 78: Current solutions
Temperature sensor with micro-controllers
  Needs battery
  Costly (~$80) each
Active battery-enabled RFID Sensor
  Intel WISP
  RFM3200 Micron
Passive RFID IC based solution
  Fixed number of temperature levels (~6)
  Costly (~$50 each) and custom reader
WISP
RFM3200
Notes: Wireless Identification and Sensing Platform

## Slide 79: Tracking within multiple tags
Notes: Then we attempt to extend We also look at tracking of tag within multiple tags. The tracking becomes worse because of the mutual coupling between tags change the observed phase pattern. However, all of the previous works actually negated the impact of mutual coupling.

## Slide 80: Mutual coupling phenomenon
Neighboring tags show
reverse phase pattern
Notes: However, there will be mutual coupling and we observe the reverse phenomenon.

## Slide 81: Multi-tag tracking algorithm sketch
Apply joint
DTW matching
Notes: We use that phase changes across neighboring tags to improve the tracking in multi-tag scenario.

## Slide 82: Azimuth and Elevation Estimation
Same optimization framework with five variables
Addressing symmetric issue (with two tags)…

## Slide 83: Gain Sampling

## Slide 84: Azimuth & Elevation Estimation Error
Median error remains within 6 degree

## Slide 85: Initialization
32 deg
9 deg
5 deg
Notes: Problem is challenging as the objective function is non-linear ... Need more description ...

## Slide 86: Key Idea
Notes: In more detail, it is explained ….

## Slide 87: Impact of dynamic multi-path
Related methods
fair relatively worse

## Slide 88: Current approaches
High-speed Camera
  Costly (~1 million dollars)
  Does not work in Non-Line-of-Sight
IMU based approaches
  Non-trivial modification in the ball
  Battery needed
WiFi / Bluetooth Beacon approaches
  Specific calibration needed
  Battery needed
  Modification needed
HawkEye
Zepp
iBall

## Slide 89: Multi-path Experiments
Both static and dynamic multi-path does not degrade performance

## Slide 90: In presence of Multi-path
Even in multi-path, shape remains similar

## Slide 91
Wireless
Capacitive
Vision
IMU
Notes: Now, let’s see what others modalities are present. To realize that goal, different types of modalities have been shown through products or research prototypes. Capacitive touch screens are present in every smartphone or tablet. Kinect and leap motion are using rgb & ir camera vision based technology to track hand movement. Wearables like smart watch is using IMUs to track different hand movement. Furthermore, 60 GHz, Wi-Fi and acoustics signals are used to track hand gestures.
Pixelsense, kinect, soli, sprout, myo, leap motion ….. IUnit)

## Slide 92: Issues with these modalities
Not easy to customize
Not low cost
Extensive training phase
Need to be recharged frequently …
Notes: However, these interaction modalities enable a suite of applications, there are few issues impacting the wide-spread adoption in smart spaces. Vision is to make everyday object touch-aware and so it will be difficult to achieve that. These UIs are difficult to customize for specific use cases and some of them require extensive training phase to be used. These UIs can also not be disposed after the use which may be needed in medical use cases and it needs to be recharged very frequently.
Low cost point creates an opportunity for massive deployment..
But, there are certain issues Coupled with device (sprout), Occlusion (vision), complex processing (soli) etc.

## Slide 93: VNA based measurements
Notes: To confirm this observation and model, we also perform vector network analyzer based experiments where we connect the tag with the VNA

## Slide 94: VNA based measurements
Notes: We touch at different positions at the RFID tag and measure the impedance and the induced phases. We observe the changes.

## Slide 95: Why does it happen ?
Coupled mutual impedance has
reverse impact in back-scattered phase
Notes: The details about the model are in the paper but the basic idea is that coupled mutual impedance has reverse impact in the backscattered phase.

## Slide 96: Custom tag tracking accuracy
Custom Tags
Error ~10 mm
Notes: We also build custom tags with loop tags and copper tapes and apply our single tag tracking algorithm. For more detailed evaluation results, please look into the paper.

## Slide 97: Key takeaways from RIO
Impedance Tracking based Touch Primitive
Mutual coupling can be exploited
Custom designed tags may enable different applications

## Slide 98: Two simple use-cases

## Slide 99: Challenges in passive RFID sensing
How can one be robust against the environmental changes ?
How to balance trade-offs like communication range and accuracy ?
How much customization is needed ?
Notes: The main challenges … We build model ..

## Slide 101: Custom Tags and Their Pattern

## Slide 102: Other Tags

## Slide 103: Algorithm: Single-Tag Touch Tracking

## Slide 104: Algorithm: Multi-Tag Touch Tracking

## Slide 105: Explanation of reverse phase trend

## Slide 106: Why does it happen ?
Notes: Negative sign …

## Slide 107: Localization error trade-off
Notes: We also look at the number of se

## Slide 108: Application performance

## Slide 109: Growing Interest in the community
LiveTag, NSDI ’18
RFWear, UbiComp’18
WiSH, MobiSys’18
Notes: Before concluding the talk, I just want to add that there is a growing interest in the community to repurpose the tags for UI after our MobiCom publication. I will not claim our influence but it is interesting ..

## Slide 110: Future works
Multi-touch tracking
General 2D gesture tracking
Tracking in different environment scenarios
Building customized tags for other use cases
Notes: However, this is just a first step realizing the ultimate goal of transforming every physical object into a possible UI. Multi –touch.. 2D gesture

## Slide 111: Spatial variation of room temperature
Notes: There are spatial variation …

## Slide 112: Constant descriptions

## Slide 113: Multiple configurations

## Slide 114: Comparison of configurations

## Slide 115: COTS tag phase change

## Slide 116: Pattern changes with other metrics

## Slide 117: Micro-benchmark results

## Slide 118: Metric parameters

## Slide 119: Tag chip-attachment choices

## Slide 120: Tag-pair phase difference metric
RTSense Tag Pair
Tag A
Tag B

## Slide 121: Other calibration techniques

## Slide 122: Impact of Calibration Location

## Slide 123: Analytical model formulae

## Slide 124: Phase pattern reflects rotation axis
Rotation Axis 1
Rotation Axis 2

## Slide 125: RSS variation provide Rotation Speed
1500 RPM
500 RPM
2000 RPM

## Slide 126: Controlled setup
Linear Track
Motor with holder

## Slide 127: Initial results
~2 Cm Error
~0.3 RPS Error
~5 Degree Error

## Slide 128: Algorithm detail of TIMU

## Slide 129: Distance change from antenna
Error remains within ~18mm

## Slide 130: Relative tilt angle change of antenna
Error remains within ~20mm

## Slide 131: Related works of RIO
RFID based gesture recognition – Data-driven learning
  ShopMiner (SenSys ‘15), FEMO (SenSys ‘15) …
RFID tag tracking – Tracks tag movement
  Tagyro (Mobicom ‘16), PolarDraw (CoNext ‘16) …
RFID based UI (Closest) – ML on a fixed set of gestures
  PaperID (CHI 2015), IDSense (CHI 2016) …
Notes: Before concluding, I just want to point out there are numerous previous attempts to use passive RFID tags as interaction units. RIO improves upon this work with high accuracy, low over head, error rate.

## Slide 132: And our interface …
Customizable and less costly
Battery-free
Supports fine-grained tracking
Multi interface support
Notes: Thus, due to the use of passive RFID tags, the interface becomes battery-free and disposable. We have also shown possible customization through custom designed tags and we have built algorithms to support fine-grained tracking. Furthermore, as the tags can be easily mapped to different objects, same interaction can also be coupled with different applications. We can discriminate and support separate interfaces within the same region.

## Slide 133: Mutual coupling reduces accuracy
Notes: Dynamic range gets reduced …

## Slide 134: This change is also present in NLoS
Behind a Wall
Behind a Door
Remains Similar
Notes: Interestingly, the phase pattern dominant in NLoS specific scenarios.