## Slide 1: Rotation Sensing Using Passive RFID Tags
Swadhin Pradhan, Shuozhe Li, Lili Qiu
07/22/2021
ACM MobiHoc 2021

## Slide 2: Sports analytics is a billion dollar industry
1.9 B
5.2 B
Annual growth rate of 22%!
Notes: 1.9 B to 5.2 B in all of the markets …

## Slide 3: Key metrics for sports analytics
Linear Speed and Direction
Rotation Speed and Direction
Rotation Axis …

## Slide 4: Current approaches
High-speed Camera
  Costly (~1 million dollars)
  Does not work in Non-Line-of-Sight
IMU based approaches
  Non-trivial modification in the ball
  Battery needed
WiFi / Bluetooth Beacon approaches
  Specific calibration needed
  Battery needed
  Modification needed
HawkEye
Zepp
iBall

## Slide 5: Can we sense rotation motion with minimal change using passive RFID tags and single reader antenna ?

## Slide 6: Our Solution: We exploit polarization property of passive RFID system
Notes: However, the future of IoT demands seamless and intuitive interface between users and the devices. In this setting, we ask that “Can we effectively transform everyday object into a touch interface ?” Can every possible item in our surrounding become a gateway to a possible interaction ? Chair, Table ..

## Slide 7: Outline
Model RSS and Phase under rotation
Estimate rotation axis assuming only rotation
Extract the rotation and translation

## Slide 8: Outline
Model RSS and Phase under rotation
Estimate rotation axis assuming only rotation
Extract the rotation and translation

## Slide 9: Modeling RSS and Phase
Exploit polarization property of RFID tag with linear antenna
Directly extract the motion states using single antenna
Polarization
Distance
Gain
Notes: K -> Polarization Loss factor (Fixed)

## Slide 10: Modeling RSS and Phase
Phase
RSS
Gain
Polarization
Polarization
Distance
Distance

## Slide 11: RSS Modeling Examples

## Slide 12: Phase Modeling Examples
For a given rotation axis, we get almost unique pattern

## Slide 13: In presence of Multi-path
Even in multi-path, shape remains similar

## Slide 14: Outline
Model RSS and Phase under rotation
Estimate rotation axis assuming only rotation
Extract the rotation and translation

## Slide 15: Estimate Rotation Axis: Problem Formulation
Given RSS and phase during a rotation, estimate the rotation axis
Model
Rotation Axis
Samples of signal (k)
For this non-linear optimization, we perform NN-driven initialization

## Slide 16: Estimate Rotation Axis: Algorithm
Usage of multiple tags
Use neural network modeling for initialization
Exploit temporal locality of movement

## Slide 17: NN-driven Initialization
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Hidden layers (ReLu)
Output
RotationX
RotationY
RotationZ
Azimuth
Elevation
Input
.
.
.
RSS and phase values for
a full rotation
Notes: Multi-layered feed-forward DNN with different number of neurons
DNN maps the phase and RSS samples to rotation axis
Training data is the combination of measurement data & synthetic data (from the analytical model and by perturbing the output values of rotation axis)

## Slide 18: Temporal Locality Idea Sketch
Use NN to get x0 (initial solution)
for i=1:L
x1 = x0 + small random noise
solve optimization using x1 as initial solution
end
Select from L candidates that has the smallest change

## Slide 19: NN-Initialization & Temporal pattern
32 deg
9 deg
5 deg
Notes: Problem is challenging as the objective function is non-linear ... Need more description ... Sketch of Rotation Estimation…

## Slide 20: Outline
Model RSS and Phase under rotation
Estimate rotation axis assuming only rotation
Extract the rotation and translation

## Slide 21: Rotation speed estimation

## Slide 22: Linear speed estimation
Compensate the
rotation axis and
speed in the
phase to extract
the linear speed

## Slide 23: Algorithm sketch
Denoised RSS and Phase Trend from the RFID Tag(s) attached to a ball
RSS and Phase Template extraction in one rotation
Peak-Valley
Detection
Rotation Axis & Rotation Speed & Azimuth & Elevation estimation
Phase
Compensation
Linear speed, distance & direction from linear phase trend, total change, & slope sign

## Slide 24
Evaluation

## Slide 25: Controlled setup
3D Printed Goniometer
Diff. Rotation Axis

## Slide 26: Controlled setup

## Slide 27: Rotation axis Estimation error
Median error remains within 5 degree

## Slide 28: Rotation axis Estimation error
Error remains within 5 degree

## Slide 29: Linear distance estimation error
Median error remains within 1 cm

## Slide 30: Azimuth & Elevation Estimation Error
Median error remains within 6 degree

## Slide 31: Multi-path Experiments
Both static and dynamic multi-path does not degrade performance

## Slide 32: Related works of TIMU
IMU enabled Approaches
  Qlipp, Zepp companies ..
IMU with UWB ranging based approaches
  iBall [NSDI 2017]
RFID tracking based approaches (Closest)
  RfIDraw (Custom hardware with multi-antenna for translation) [SigComm ‘14]
  RFind (Offline high-bandwidth approach with USRP for localization) [MobiCom ‘17]
  Tagyro (Multiple antennas to extract static orientation) [Mobicom ‘16] …
Notes: Add differences .. A bunch of translation sensing work and … Tagyro (static orientation)… Rotation sensing (Search)… Translation sensing.. Orientation sensing.. But Not Rotation Sensing …

## Slide 33: Key takeaways of TIMU
Polarization can be exploited for motion sensing
TIMU can sense different motion states w/o tracking
First RFID-based single antenna motion sensing system

## Slide 34: Thanks for listening

## Slide 35: Backup Slides

## Slide 36: Key Idea Roadmap
Model RSS and Phase under rotation
Estimate the rotation axis using an optimization framework
Address the non-convexity of the optimization through:
  Usage of multiple tags
  Leveraging neural network modeling for initialization
  Exploiting temporal locality of movement
Extract the translation from the phase change

## Slide 37: Key Idea
Notes: In more detail, it is explained ….

## Slide 38: Gain Sampling

## Slide 39: Algorithm detail of TIMU

## Slide 40: Metrics of interest in sports analytics
Ball Motion Analytics in Bat or/and Ball sports
Baseball
Cricket
Basketball
Can be used in coaching and performance improvement

## Slide 41: Estimating Rotation Axis
Estimating the rotation axis (and then azimuth and elevation) using an optimization framework
Address the non-convexity of the optimization:
  Usage of multiple tags
  Leveraging neural network modeling for initialization
  Exploiting temporal locality of movement

## Slide 42: Estimating Rotation Axis
Estimating the rotation axis (and then azimuth and elevation) using an optimization framework
Address the non-convexity of the optimization:
  Usage of multiple tags
  Leveraging neural network modeling for initialization
  Exploiting temporal locality of movement