## Slide 1: Revisiting Transport Congestion Control
Jian He
UT Austin

## Slide 2: Why is Congestion Control necessary?
Data
Packets
ACK
Congested
Link
Congested link vs. reliability: long queuing delay, packet loss
But, can delay or packet loss always well explain congestion?

## Slide 3: Can we distinguish congestion reasons?
Congestion related signals:
- packet loss: duplicate ACKs, retransmission timeout
(TCP Reno, TCP Cubic)
- round-trip delay: TCP packet RTT
(TCP Vegas, FAST TCP, Compound TCP)
- queue size: explicit congestion notification(ECN)
(DCTCP)

## Slide 4: Existing TCP Variants
TCP
Throughput-Latency Tradeoff Exploration
[Remy SIGCOMM’13]
Datacenter TCP
Tail performance[TIMELY SIGCOMM’15], New Architectures[R2C2 SIGCOMM’15] RDMA[DCQCN SIGCOMM’15]
Persistently High Performance
Large flows[PCC NSDI’15]
Highly-variant network condition
Cellular transport[Verus SIGCOMM’15, Sprout NSDI’13]
Reducing Start-up Delay
[Halfback CoNext’15], [RC3 NSDI’14]
Performance interference for competing flows
Application Heterogeneity[QJUMP NSDI’15]

## Slide 5: TCP Evolution
Application
TCP
IP
Link
Hardware
Application Sensing Layer
Networking Sensing Layer
Application-Specific
Performance Requirements
Network Condition

## Slide 6: Optimizing Datacenter Transport Tail Performance
Mittal, Radhika, et al. "TIMELY: RTT-based congestion control for the datacenter."
In ACM SIGCOMM 2015.

## Slide 7: Why does tail performance matter?
…
TCP Incast: many servers reply the client simultaneously
All replies should meet their deadlines.
Datacenter transport must deliver high throughput(>>Gbps)
and utilization with low delay(<<msec).

## Slide 8: Hardware Assisted RTT Measurement
Why was RTT not widely used?
RTT-based congestion control performed poorly at WANs.
Highly noisy RTT estimation(system kernel scheduling, etc.)
Datacenter RTT measurement needs ms-level granularity.
Hardware timestamp and hardware acknowledgement
can significantly remove noise.

## Slide 9: RTT As a Congestion Control Signal
Multi-bit signal
Single-bit signal
ECN can not reflect the extent of end-to-end latency
inflated by network queuing, due to traffic priorities,
multiple congested switches, etc.

## Slide 10: RTT Correlates with Queuing Delay

## Slide 11: TIMELY Framework

## Slide 12: RTT Measurement
tsend
tcompletion
ACK Turnaround Time
Serialization Delay
Propagation &
Queuing Delay
One RTT for one segment (NIC Offload)
Hardware ACKs make ACK turnaround time ignorable
RTT = Propagation + Queuing Delay
= tcompletion – tsend – segment_size/NIC_line_rate
RTT

## Slide 13: Transmission Rate Control
Rate Controller
Message to
be sent
Segments
RTT
Estimation
Transmission
Queue
Insert delay between
segments
Target rate is determined by segment size and delay
between segments

## Slide 14: Rate vs. Window
Segment size as high as 64KB.
(32us RTT x 10Gbps) = 40KB window size
40KB < 64KB: Window makes no sense

## Slide 15: Rate Update

## Slide 16: Evaluation

## Slide 17
Datacenter Transport for Emerging Architectures
Costa, Paolo, et al. "R2C2: A Network Stack for Rack-scale Computers."
In ACM SIGCOMM 2015.

## Slide 18: Rack-Scale Computing
Building Block for future datacenters
High BW low latency network
Direct-connected topology

## Slide 19: Rack-Scale Network Topology
3D Torus
Fat-tree Topology
Distributed switches(each node works as a switch)
High path diversities

## Slide 20: Broadcasting-Assisted Rack Congestion Control
Broadcast flow information(e.g., start time, finish time)
Each node has a global view of the network
Locally optimize flow rate with the global view
Broadcasting overhead is
low(around 1.3%).

## Slide 21: Evaluation

## Slide 22
Congestion Control for
RDMA-enabled Datacenters
Zhu, Yibo, et al. "Congestion Control for Large-Scale RDMA Deployments.”
In ACM SIGCOMM, 2015.

## Slide 23: Congestion Spreading in Lossless Networks
PAUSE
PAUSE
PAUSE
PAUSE
PAUSE
PAUSE
PAUSE
PAUSE
PAUSE
PAUSE
Port-based congestion control incurs congestion spreading
DCQCN: incorporating explicit congestion notification to
support flow-based congestion control

## Slide 24
Wireless Congestion Control
Zaki, Yasir, et al. "Adaptive Congestion Control for
Unpredictable Cellular Networks.“ In SIGCOMM 2015.

## Slide 25: What do Cellular Traffic Look Like?
Burst Scheduling
Competing Traffic

## Slide 26: What do Cellular Traffic Look Like?
Channel Unpredictability

## Slide 27: Verus Protocol
Epoch i
Epoch i+1
Epoch: a short period of time (e.g., 5 ms)
Sending window is updated at each epoch.
Sending window represents the number packets in flight.
Sending window
Wi
Sending window
Wi+1

## Slide 28: Verus Overview
Delay Estimator: estimate delay in the
future based on the changes of delay
Delay Profiler: record the relationship of
delay-sending window
Window Estimator: estimate the sending
window for the next epoch
Packet Scheduler: calculate the number
packets to be sent in the next epoch
Go to
next epoch

## Slide 29: Delay Estimation
Epoch i-1
Epoch i
Dmax,i-1
Dmax,i
Dmax,i =
alpha x
+ (1-alpha) x
∆Di = Dmax,i -Dmax,i-1
Dest,i
•
Dest,i+1
•
•
∆Di<=0
∆Di>0
Time
Estimated
Delay

## Slide 30: Window Update
Delay-Window Profile: updated based on historical data
Each epoch can contribute many points to the profile.
Profile is initialized using data in the slow-start phase.

## Slide 31: Packet Scheduler
Epoch i
Epoch i+1
Sending window
Wi
Sending window
Wi+1
How many packets to be sent in current epoch?
Si+1 = max[0, (Wi+1 + ((2-n)/(n-1))*Wi)]
n is the number of epochs over the current estimated RTT

## Slide 32: Loss Handling
Epoch i
Epoch i+1
Sending window
Wi
Multiplicative Decrease
Wi+1 = M * Wi
Stop updating delay profile during the loss recovery phase

## Slide 33: Evaluation

## Slide 34
Thanks!